## Slide 1: Intro to LabVIEW
http://workshop.frclabviewtutorials.com

## Slide 2: Front Panel
Controls
Indicators

## Slide 3: Block Diagram
Controls
Indicators
Terminals

## Slide 4: Demo
Adding controls and indicators

## Slide 5: Demo
Adding controls and indicators

## Slide 6: Data Flow
LabVIEW follows a dataflow model for running Vis
A node executes only when data is available at all of its required input terminals.
A node supplies data to the output terminals only when the node finishes execution.
Notes: When a node executes, it produces output data and passes the data to the next node in the dataflow path.
The movement of data through the nodes determines the execution order of the VIs and functions on the block diagram.
LabVIEW does NOT use a control flow program execution model like Visual Basic, C++, JAVA, and most other text-based programming languages. In a control flow model, the sequential order of program elements determines the execution order of a program.

## Slide 7: Demo - Setting a motor
Read Joystick
Set Drive motors

## Slide 8: Demo - Setting a motor
Read Joystick
Set Drive motors

## Slide 9: Exercise
Drive a motor.pdf

## Slide 10: Case Structures
Have two or more sub diagrams or cases.
Use an input value to determine which case to execute.
Execute and display only one case at a time.
Are similar to case statements or if...then...else statements in text-based programming languages.
Notes: Casestructure.vi and select.vi

## Slide 11: Case Structures
Input and Output Tunnels
  You can create multiple input and output tunnels.
  Input tunnels are available to all cases if needed.
  You must define each output tunnel for each case.*

## Slide 12: Repetition
While Loop

## Slide 13: Repetition
While Loop
  Iteration terminal
    Returns number of times loop has executed.
    Is zero-indexed.
Iteration Terminal

## Slide 14: Repetition
While Loop
  Conditional terminal
    Defines when the loop stops.
    Has two options.
      Stop if True
      Continue if True
Conditional Terminal
Iteration Terminal

## Slide 15: Repetition
While Loop
  Tunnels transfer data into and out of structures.

## Slide 16: Repetition
While Loop
  Tunnels transfer data into and out of structures.
  Data pass out of a loop after the loop terminates.

## Slide 17: Repetition
While Loop
  Tunnels transfer data into and out of structures.
  Data pass out of a loop after the loop terminates.
  When a tunnel passes data into a loop, the loop executes only after data arrives at the tunnel.

## Slide 18: Repetition
While Loop - Demo

## Slide 19: Exercise – While Loops
While Loops.pdf
Notes: pp. 62-75
How many times is the Number of Indicator updated? Why?
Once, because the output tunnel on the While Loop will output only a single value once the While Loop has finished executing.

## Slide 20: Exercise – While Loops
How many times is the Number of Iterations indicator updated? Why?
Notes: pp. 62-75
How many times is the Number of Indicator updated? Why?
Once, because the output tunnel on the While Loop will output only a single value once the While Loop has finished executing.

## Slide 21: Repetition
While Loop
For Loop

## Slide 22: Repetition
While Loop
For Loop
  Count Terminal

## Slide 23: Repetition
Comparison
  Description
    For the following scenarios, decide whether to use a While Loop or a For Loop.

## Slide 24: Repetition
Comparison
  Description
    For the following scenarios, decide whether to use a While Loop or a For Loop.
  Scenario 1
    Acquire sensor data in a loop that runs once per second for 15s (autonomous).
    1. If you use a While Loop, what is the condition that you need to stop the loop?
    2. If you use a For Loop, how many iterations does the loop need to run?
    3. Is it easier to implement a For Loop or a While Loop?

## Slide 25: Repetition
Comparison
  Description
    For the following scenarios, decide whether to use a While Loop or a For Loop.
  Scenario 1
    Acquire sensor data in a loop that runs once per second for 15s (autonomous).
    1. If you use a While Loop, what is the condition that you need to stop the loop?
    2. If you use a For Loop, how many iterations does the loop need to run?
    3. Is it easier to implement a For Loop or a While Loop?
  Scenario 2
    Acquire gyro until it reads less than 15°
    1. If you use a While Loop, what is the condition that you need to stop the loop?
    2. If you use a For Loop, how many iterations does the loop need to run?
    3. Is it easier to implement a For Loop or a While Loop?

## Slide 26: Repetition
Comparison
  Scenario 3
    Read both joysticks until they are both negative
    1. If you use a While Loop, what is the condition that you need to stop the loop?
    2. If you use a For Loop, how many iterations does the loop need to run?
    3. Is it easier to implement a For Loop or a While Loop?

## Slide 27: Repetition
Comparison
  Scenario 3
    Read both joysticks until they are both negative
    1. If you use a While Loop, what is the condition that you need to stop the loop?
    2. If you use a For Loop, how many iterations does the loop need to run?
    3. Is it easier to implement a For Loop or a While Loop?
  Scenario 4
    Control a motor ramp starting at zero, increasing incrementally by 0.01 every second, until the output value reaches 1
    1. If you use a While Loop, what is the condition that you need to stop the loop?
    2. If you use a For Loop, how many iterations does the loop need to run?
    3. Is it easier to implement a For Loop or a While Loop?

## Slide 28: FRC Arhitecture
Begin

## Slide 29: FRC Arhitecture
Begin
Notes: Show it

## Slide 30: FRC Arhitecture
Begin
  Create references for all joysticks, motors, and sensors
  Runs at power up

## Slide 31: FRC Arhitecture
Begin
Teleop

## Slide 32: FRC Arhitecture
Begin
Teleop

## Slide 33: FRC Arhitecture
Begin
Teleop
  Primarily used to read joysticks and set drive motors and actuators
  Only runs while Teleop enabled

## Slide 34: FRC Arhitecture
Begin
Teleop
Autonomous

## Slide 35: FRC Arhitecture
Begin
Teleop
Autonomous

## Slide 36: FRC Arhitecture
Begin
Teleop
Autonomous
  Runs when Autonomous is enabled

## Slide 37: FRC Arhitecture
Begin
Teleop
Autonomous
Timed Tasks

## Slide 38: FRC Arhitecture
Begin
Teleop
Autonomous
Timed Tasks

## Slide 39: FRC Arhitecture
Begin
Teleop
Autonomous
Timed Tasks
  Runs once enabled (during both auto and teleop)

## Slide 40: FRC Deploying Code
Run From Main
Notes: Open Main.vi (from project) – click the run buton

## Slide 41: FRC Deploying Code
Run From Main
Deploy
Notes: Deploying the robot code puts it on the robot – causing it to take effect on next reboot (or after Run as startup)

## Slide 42: FRC Deploying Code
Run From Main
Deploy
Run as Startup
Notes: Run as startup puts the code on the roborio in a temporary location and starts it running (does not persist across reboots).

## Slide 43: Debugging Techniques
Correcting Broken VI’s

## Slide 44: Debugging Techniques
Correcting Broken VI’s
  Broken Wires Exist (e.g.)
    You wired a Boolean control to a String indicator.
    You wired a numeric control to a numeric control.
Notes: Untitled1.vi

## Slide 45: Debugging Techniques
Correcting Broken VI’s
  Broken Wires Exist (e.g.)
    You wired a Boolean control to a String indicator.
    You wired a numeric control to a numeric control.
  A required block diagram terminal is unwired.
Notes: Untitled1.vi

## Slide 46: Debugging Techniques
Correcting Broken VI’s
  Broken Wires Exist (e.g.)
    You wired a Boolean control to a String indicator.
    You wired a numeric control to a numeric control.
  A required block diagram terminal is unwired.
  A subVI is broken
Notes: Untitled1.vi

## Slide 47: Debugging Techniques
Correcting Broken VI’s
Correcting Dataflow
  Execution Highlighting
  Single-Stepping & Breakpoints
  Probes
Notes: untitled1

## Slide 48: Debugging Techniques
Correcting Broken VI’s
Correcting Dataflow
  Are there any unwired or hidden subVIs?
  Is the default data correct?
  Does the VI pass undefined data?
  Are numeric representations correct?
  Are nodes executed in the correct order?

## Slide 49: Terminals and LabVIEW datatypes
Notes: Terminal colors, text, arrow direction, and border thickness all provide visual information about the terminal.
For example, Orange represents floating point numbers. DBL indicates a double-precision floating point number.
Terminals with thick borders with arrows on the right are control terminals. Terminals with thin borders with arrows on the left are indicator terminals.

## Slide 50: Data Feedback in Loops
Shift Registers
  When programming with loops, you often need to know the values of data from previous iterations of the loop.
  Shift registers transfer values from one loop iteration to the next.

## Slide 51: Documentation
Free Labels

## Slide 52: Documentation
Free Labels
  Describe algorithms.
  Have pale yellow backgrounds.
  Double-click in any open space to create.

## Slide 53: Documentation
Free Labels
  Describe algorithms.
  Have pale yellow backgrounds.
  Double-click in any open space to create.

## Slide 54: Documentation
Free Labels
Owned Labels
  Explain data contents of wires and objects.
  Move with object.
  Have transparent backgrounds.
  Select Visible Items»Label from the shortcut menu to create.

## Slide 55: Documentation
Free Labels
Owned Labels
  Explain data contents of wires and objects.
  Move with object.
  Have transparent backgrounds.
  Select Visible Items»Label from the shortcut menu to create.

## Slide 56: Documentation
Free Labels
Owned Labels
Sub diagram Labels
  Case Structures

## Slide 57: Documentation
Free Labels
Owned Labels
Sub diagram Labels
  Case Structures
  Loops

## Slide 58: Documentation
Free Labels
Owned Labels
Sub diagram Labels
White Papers

## Slide 59: Documentation
Free Labels
Owned Labels
Sub diagram Labels
White Papers

## Slide 60: Keyboard Shortcuts
CTRL + u = diagram cleanup
Right Click = palette
CTRL + Space = quick drop
CTRL + e = switch window
CTRL + Shift + e = activate project window
CTRL + r = Run
CTRL + t = split window